## Slide 1
main_drive.m
主驱动脚本 | Main driver script
中文
设置本次算例并启动整个计算。
• 选择条材或杆材。
• 按需覆盖本次运行参数。
• 调用统一入口，保留计算结果。
English
Configure a case and start the calculation.
• Select FRP strips or rods.
• Optionally override parameters for this run.
• Call the main entry and retain the results.
启动与输入 / Setup
01/16
Notes: main_drive.m
设置本次算例并启动整个计算。
Configure a case and start the calculation.

## Slide 2
parameters.m
默认参数 | Default parameters
中文
集中提供模型和计算的默认设置。
• 定义几何、材料、黏结和荷载参数。
• 设置循环数及数值控制参数。
• 设置绘图和文件导出选项。
English
Provide the default model and analysis settings.
• Define geometry, materials, bond and loading parameters.
• Set cycle limits and numerical controls.
• Set plotting and file-export options.
启动与输入 / Setup
02/16
Notes: parameters.m
集中提供模型和计算的默认设置。
Provide the default model and analysis settings.

## Slide 3
read_and_calculate.m
统一入口 | Calculation entry point
中文
连接参数读取、疲劳计算和结果导出。
• 读取默认参数并应用本次覆盖值。
• 调用疲劳计算主函数。
• 根据开关调用绘图与导出。
English
Link parameter loading, fatigue analysis and result export.
• Load defaults and apply run-specific overrides.
• Call the fatigue analysis controller.
• Trigger plotting and export when enabled.
启动与输入 / Setup
03/16
Notes: read_and_calculate.m
连接参数读取、疲劳计算和结果导出。
Link parameter loading, fatigue analysis and result export.

## Slide 4
prepare_parameters.m
参数检查与几何准备 | Parameter checks and geometry
中文
检查输入并建立求解需要的几何信息。
• 检查参数范围和相互关系。
• 确定裂缝与FRP筋的真实交点。
• 计算两侧锚固长度及穿缝箍筋位置。
English
Check inputs and prepare the geometry used by the solver.
• Check parameter ranges and consistency.
• Locate actual crack–FRP intersections.
• Calculate anchor lengths and intersecting stirrup positions.
模型准备 / Model preparation
04/16
Notes: prepare_parameters.m
检查输入并建立求解需要的几何信息。
Check inputs and prepare the geometry used by the solver.

## Slide 5
fatigue_calculate.m
疲劳计算总控制 | Fatigue analysis controller
中文
组织峰谷平衡、损伤更新和循环推进。
• 初始化历史并求初始峰谷状态。
• 提出候选循环块，必要时减半重试。
• 接受有效状态并记录结果和停止原因。
English
Coordinate load-state equilibrium, history updates and cycle progression.
• Initialize history and solve the initial peak and valley states.
• Propose cycle blocks and halve them when required.
• Accept valid states and record results and stop reasons.
循环控制 / Cycle control
05/16
Notes: fatigue_calculate.m
组织峰谷平衡、损伤更新和循环推进。
Coordinate load-state equilibrium, history updates and cycle progression.

## Slide 6
capacity_scan.m
初始抗剪响应扫描 | Initial shear-response scan
中文
提供当前历史下的可选静力路径诊断。
• 按递增裂缝位移计算抗剪响应。
• 保留成功点的加载历史。
• 记录有效采样峰值与数值失败点。
English
Provide an optional static-path diagnostic for the current history.
• Sample shear resistance at increasing crack displacement.
• Carry forward successful loading history.
• Record the sampled peak and numerical failures.
静力诊断 / Static diagnostic
06/16
Notes: capacity_scan.m
提供当前历史下的可选静力路径诊断。
Provide an optional static-path diagnostic for the current history.

## Slide 7
state.m
抗剪平衡求解 | Shear-equilibrium solver
中文
寻找满足目标剪力的裂缝竖向位移差。
• 设置峰值或谷值的搜索范围。
• 扫描并二分搜索有效平衡根。
• 返回平衡响应或具体求解诊断。
English
Find the vertical crack jump that balances the target shear.
• Set the peak- or valley-state search interval.
• Scan and bisect to find a valid equilibrium root.
• Return the balanced response or a specific diagnostic.
平衡求解 / Equilibrium
07/16
Notes: state.m
寻找满足目标剪力的裂缝竖向位移差。
Find the vertical crack jump that balances the target shear.

## Slide 8
trial.m
单次抗剪响应计算 | Single trial response
中文
在给定裂缝位移下计算各项抗剪贡献。
• 计算混凝土和箍筋贡献。
• 逐根求FRP锚固响应并检查筋失效。
• 汇总FRP竖向力与总抗剪力。
English
Evaluate shear-resistance components at a prescribed crack jump.
• Calculate concrete and stirrup contributions.
• Solve each FRP anchor response and check bar failure.
• Sum FRP vertical forces and total shear resistance.
局部力学 / Mechanical response
08/16
Notes: trial.m
在给定裂缝位移下计算各项抗剪贡献。
Evaluate shear-resistance components at a prescribed crack jump.

## Slide 9
crack_deformation.m
裂缝变形分布 | Crack-deformation profiles
中文
由裂缝竖向位移尺度得到指定的变形分布。
• 建立沿裂缝高度的形状分布。
• 计算法向张开和切向滑移。
• 返回竖向、水平位移差及绘图数据。
English
Generate prescribed crack profiles from the vertical crack-jump scale.
• Define the profile along the crack height.
• Calculate normal opening and tangential sliding.
• Return vertical/horizontal jumps and profile data.
局部力学 / Mechanical response
09/16
Notes: crack_deformation.m
由裂缝竖向位移尺度得到指定的变形分布。
Generate prescribed crack profiles from the vertical crack-jump scale.

## Slide 10
bond_strength.m
黏结峰值疲劳退化 | Fatigue degradation of bond peaks
中文
按节点局部循环数计算退化后的黏结峰值。
• 检查局部循环历史。
• 区分杆材和条材的退化系数。
• 返回非负的节点峰值黏结应力。
English
Calculate degraded peak bond stress from local cycle counts.
• Check the local cycle history.
• Use the rod- or strip-specific degradation coefficient.
• Return nonnegative nodal peak bond stresses.
界面疲劳 / Interface fatigue
10/16
Notes: bond_strength.m
按节点局部循环数计算退化后的黏结峰值。
Calculate degraded peak bond stress from local cycle counts.

## Slide 11
anchorage.m
双侧锚固求解 | Two-sided anchorage solver
中文
求裂缝两侧锚固段的滑移和筋力。
• 组装杆单元和黏结刚度。
• 迭代满足两侧滑移协调与力平衡。
• 返回局部应力、应变及脱黏状态。
English
Solve slip and bar force on both sides of the crack.
• Assemble bar-element and bond stiffness.
• Iterate to satisfy slip compatibility and force balance.
• Return local stresses, strains and debonding status.
锚固与黏结 / Anchorage and bond
11/16
Notes: anchorage.m
求裂缝两侧锚固段的滑移和筋力。
Solve slip and bar force on both sides of the crack.

## Slide 12
anchor_mesh.m
锚固网格 | Anchorage mesh
中文
为一个锚固段建立一维数值离散。
• 按设定单元数生成节点位置。
• 计算各单元长度。
• 提供梯形积分的节点权重。
English
Create a one-dimensional discretization of an anchor segment.
• Generate nodes using the specified element count.
• Calculate element lengths.
• Provide nodal trapezoidal integration weights.
锚固与黏结 / Anchorage and bond
12/16
Notes: anchor_mesh.m
为一个锚固段建立一维数值离散。
Create a one-dimensional discretization of an anchor segment.

## Slide 13
bond.m
黏结本构关系 | Bond constitutive relation
中文
根据历史最大滑移计算黏结包络和刚度。
• 判断弹性、软化或残余阶段。
• 计算包络应力及割线刚度。
• 供锚固求解计算当前黏结应力。
English
Evaluate the bond envelope and stiffness from maximum slip history.
• Identify the elastic, softening or residual branch.
• Calculate envelope stress and secant stiffness.
• Supply stiffness for current anchor-stress evaluation.
锚固与黏结 / Anchorage and bond
13/16
Notes: bond.m
根据历史最大滑移计算黏结包络和刚度。
Evaluate the bond envelope and stiffness from maximum slip history.

## Slide 14
active_nodes.m
疲劳活跃节点判断 | Active fatigue-node selection
中文
判断哪些节点可以累计本步疲劳循环。
• 检查滑移阈值和历史激活记录。
• 检查峰谷滑移差是否超过容差。
• 返回活跃标志及滑移差。
English
Identify nodes eligible to accumulate local fatigue cycles.
• Check the slip threshold and previous activation.
• Check that the peak–valley slip range exceeds tolerance.
• Return active-node flags and slip ranges.
界面疲劳 / Interface fatigue
14/16
Notes: active_nodes.m
判断哪些节点可以累计本步疲劳循环。
Identify nodes eligible to accumulate local fatigue cycles.

## Slide 15
save_snapshot.m
计算快照整理 | Response snapshot assembly
中文
整理选定循环数的响应和局部场数据。
• 按筋、锚固侧和节点整理局部场。
• 记录箍筋响应及裂缝变形分布。
• 返回快照结构体，供后续绘图和导出。
English
Assemble response and local-field data at selected cycle counts.
• Organize fields by bar, anchor side and node.
• Record stirrup responses and crack profiles.
• Return snapshot data for plotting and export.
结果处理 / Results
15/16
Notes: save_snapshot.m
整理选定循环数的响应和局部场数据。
Assemble response and local-field data at selected cycle counts.

## Slide 16
export_results.m
绘图与结果导出 | Plotting and result export
中文
将计算结果转换为图像和可读取的数据文件。
• 绘制循环历史、几何和局部场。
• 导出MAT、CSV和PNG。
• 记录计算状态、残差及失效信息。
English
Convert analysis results into figures and readable data files.
• Plot cycle histories, geometry and local profiles.
• Export MAT, CSV and PNG files.
• Record analysis status, residuals and failure information.
结果处理 / Results
16/16
Notes: export_results.m
将计算结果转换为图像和可读取的数据文件。
Convert analysis results into figures and readable data files.